## Slide 1
AI Data Center Cooling Loop Risk Map
From sensor drift to thermal throttling: where operations teams lose margin
1
Sensor Layer
Monitor what matters. Calibrate. Trust but verify.
Temperature
Inlet / Outlet / dT
Pressure
Supply / Return
Flow Rate
Per loop / Per rack
Power
Pumps / Chillers / IT
Calibration
Critical: 30 days
Health Summary
Sensors
1,248
Healthy 92.1%
Warning 6.3%
Critical 1.6%
Top Drift Risks (30d)
dT sensor drift
0.9 C
Pressure offset
1.3 psi
Flow meter bias
4.1%
Ambient probe
0.6 C
Cooling Loop Overview (Primary Loop)
Chiller Plant
*
*
*
Chiller 1
COP 5.6
Load 78%
Chiller 2
COP 5.1
Load 62%
Supply
7.2 C
2.1 bar
Supply Header
Pump A
Speed 78%
Flow 245 L/s
Pump B
Speed 62%
Flow 198 L/s
Rack Rows
Return
16.4 C
1.8 bar
Return Header
Expansion Tank
Level 68%
N2 1.0 bar
BMS / DCIM
Closed-loop Control & Alerts
2
Pump & Chiller Loop
Keep the loop stable and efficient.
Loop KPIs
Target
Delta
Supply Temp
7.2 C
7.0
+0.2
Return Temp
16.4 C
17.0
-0.6
Delta T
9.2 C
10.0
-0.8
Flow Rate
443 L/s
450
-7
Pressure
2.1 bar
2.2
-0.1
Chiller Efficiency
COP (Avg)
6.0
4.5
3.0
00:00 06:00 12:00 18:00 24:00
3
Rack Heat Load
Understand heat where it is generated.
Heat Map (Top View)
1
2
3
4
5
6
7
8
9
10
11
12
R1
R2
R3
R4
R5
kW / rack
>30
24
18
12
6
<3
Load Distribution
High (> 20 kW)
21%
Med (10-20 kW)
47%
Low (< 10 kW)
32%
Load
Heat distribution
Thermal Headroom
Min
4.1 C
Avg
8.6 C
Max
13.2 C
Total IT Load
2,846 kW
Peak Rack
R3-06
28.7 kW
Hotspots
7
Risk Register (Top 5)
#
Risk
Category
Likelihood
Impact
Risk
Leading Indicators
Mitigation
Owner
Status
1
Sensor Drift
Monitoring
15
dT variance up, calibration due
Calibrate sensors, enforce cadence
NOC
Warning
2
Pump Degradation
Mechanical
12
Flow margin down, vibration up
Service pump, monitor vibration
DC Ops
Warning
3
High Return Temp
Thermal
16
Return temp up, headroom down
Increase flow, check load balance
DC Ops
Critical
4
Low Flow Filter Clog
Maintenance
8
dP across filter up, flow down
Clean/replace filters
Facilities
Warning
5
Chiller Efficiency Drop
Efficiency
8
COP down, kW/ton up
Condenser clean, setpoint check
Facilities
Warning
System KPIs (Real-time)
PUE
1.28
WUE
0.18 L/kWh
DCiE
0.78
IT Load
2,846 kW
4
Response Playbook
Detect -> Diagnose -> Decide -> Act -> Verify
1
Detect
Alarm / Anomaly / Trend
Validate sensor health
2
Diagnose
Isolate loop / zone
Check recent changes
3
Decide
Impact vs. urgency
Choose mitigation path
4
Act
Execute runbook
Communicate & log
5
Verify
Confirm recovery
Post-incident review
Runbook Shortcuts
+
High Return Temp
Increase flow / Capacity
+
Low dT
Check flow / Bypass
+
Low Flow
Pump / Valve / Filter
+
High Pressure
Leak / Blockage
+
Temp Throttling
Load shed / Policy
+
Escalation
NOC -> DC Ops -> Vendor
Active Alerts
3 Critical 8 Warning
Next Maintenance
Filters: 2 days Pumps: 12 days
Weather Impact
High ambient Risk up
Capacity Headroom
Chiller: 22% Power: 18%
Synthetic validation slide - Editable PPTX reconstruction example -
Slide 001